## Slide 1: NETWORK INSTALLATION

## Slide 2: TOPIC
INTRODUCTION TO LAN

## Slide 3: OBJECTIVES:
By the end of the lesson the student will be able to:
Define LAN.
Outline the characteristics of LAN.
Identify the hardware components of LAN.
State the functions of the hardware components of LAN.

## Slide 4: Meaning of lan
A local area network (LAN) is a group of computers and associated devices that share a common communications line or wireless link to a server.
Typically, a LAN encompasses computers and peripherals connected to a server within a distinct geographic area such as an office or a commercial establishment.

## Slide 5: Meaning of lan (CONT.)
Computers and other mobile devices use a LAN connection to share resources such as a printer or network storage.
Computers and other mobile devices use a LAN connection to share resources such as a printer or network storage.

## Slide 6: Meaning of lan (CONT.)
LAN networking comprises cables, switches, routers and other components that let users connect to internal servers, websites and other LANs via wide area networks.
Ethernet and Wi-Fi are the two primary ways to enable LAN connections.
Ethernet is a specification that enables computers to communicate with each other.

## Slide 7: Meaning of lan (CONT.)
Wi-Fi uses radio waves to connect computers to the LAN.
Other LAN technologies, including Token Ring, Fiber Distributed Data Interface and ARCNET, have lost favor as Ethernet and Wi-Fi speeds have increased.

## Slide 8: Meaning of lan (CONT.)
Traditional LANs run at speeds of 10 Mbps to 100 Mbps, have low delay (microseconds or nanoseconds) and make very few errors.
Newer LANs operate at up to 10 Gbps.

## Slide 9: CHARACTERISTICS OF A LAN
It is limited to a small geographical area (less than 1 km radius).
In LAN you can run multiple devices to share a transmission medium.
LAN support a variety of communications transmission medium such as a Ethernet cable (thin cable, thick cable, and twisted pair), fiber and wireless transmission.

## Slide 10: CHARACTERISTICS OF A LAN
Data error rate is very less since data is transferred to limited distance.
Only limited number of computers are connected in a LAN network.
It provides high speed data transfer rate.
It not expensive (low cost).
It installation is very simple.

## Slide 11: HARDWARE COMPONENTS OF LAN
Communication Media
Network Interface Card (NIC)
Bridge
Router
Gateway

## Slide 12: Functions Of Communication Media
It is used to transfer data from one computer to another computer.
Low-cost LANs are connected with twisted pair cables.
Many LANs use coaxial or fiber-optic cables.
Some LANs use wireless transmission media instead of cable.

## Slide 13: Functions of Network Interface Card (NIC)
It is also known as network adapter.
It is a device that physically connects each computer to a networks.
It may have a connector for accepting a cable, or an aerial for wireless transmission and reception, and the associated circuitry.
It responds to traffic addressed to a network address for either the NIC or the computer as a whole.

## Slide 14: Functions Of Bridge
It is a device that connects two network segments.
It is used to connect similar types of networks.
Network segmentation breaks down a large, congested network into an aggregation of smaller, more efficient networks.

## Slide 15: Functions Of Router
It is a device that connects multiple networks using similar or different protocols.
A router uses routing table to determine where to forward packets.

## Slide 16: Functions Of Gateway
It is a device that connects two or more networks with different types of protocols.